## Slide 1: Anaesthesia Machine
Done By:
Bilal Al-Manasyeh
Anas Satari
Qabas Al-Hawamdeh

## Slide 2: Anaesthesia Machine
In recent years, the anaesthesia machine has been renamed the anaesthesia delivery system, or anaesthesia workstation because modern devices do more than simply delivering inhalational anaesthesia.
The term ‘‘Anaesthesia Machine’’ specifically refers to that component of the anaesthesia delivery system that precisely mixes the compressed and vaporized gases that are inhaled to control patient’s level of consciousness , analgesia or both during surgical procedures.

## Slide 3: Purposes of anaesthesia machine
Provides oxygen
Accurately mixes anaesthetic gases & vapours
Enables patient ventilation
Minimizes anaesthesia related risks to patients & staff

## Slide 4: Type of anaesthesia machine
Continuous-flow anaesthetic machine or Boyle's machine : which is designed to provide an accurate supply of medical gases mixed with an accurate concentration of anaesthetic vapour, and to deliver this continuously to the patient at a safe pressure and flow.
Intermittent-flow anaesthetic machines : which provide gas flow only on demand when triggered by the patient's own inspiration.

## Slide 5: Component of anaesthesia machine
Oxygen source
Flowmeter
Vaporizer
Patient breathing circuit
Scavenging system
Heads-up display

## Slide 6: Medical gases
The medical gases commonly used in operating rooms are oxygen, nitrous oxide, and air.
Gases used in anaesthesia are usually supplied under high pressure either in cylinders or as a piped gas supply.

## Slide 7: Characteristics of Medical Gas Cylinders

## Slide 9: Pipelines
Medical gases are delivered from their central supply source to the operating room through a piping network.
The tubing is colour-coded and connects to the anaesthesia machine through a non-interchangeable diameter-index safety system (DISS) fitting that prevents incorrect hose attachment.
The anaesthetist should check that the pipeline pressure displayed on the anaesthetic machine should indicate 400 kPa.

## Slide 11: Flowmeters and gas flow regulation
Valves
Needle valves
As the valve is opened, the orifice around the needle becomes larger and flow increases.

## Slide 12: Flowmeters
Tapered glass tube containing a bobbin or ball, which floats on the stream of moving gas.
Flowmeters are specifically constructed for each gas, since the flow rate depends on both the viscosity and density of the gas.
Inaccuracy in flowmeters are due to:
- The tube not being vertical.
- Back-pressure, from for example, a ventilator.
- Static electricity causing the float to stick to the tube.
- Dirt causing the float to stick to the tube

## Slide 13: Bobbins and balls
Bobbin flowmeter, reading 2 L/min Ball-float flowmeter, reading 2 L/min

## Slide 14: Vapourisers
The purpose of an anaesthetic vaporiser is to produce a controlled and predictable concentration of anaesthetic vapour in the carrier gas passing through the vaporiser.
Most vaporisers are of the plenum type, which consists of a vaporising chamber containing the liquid anaesthetic, and a bypass.
Gas passing through the vaporising chamber volatilises the anaesthetic and is then mixed with the anaesthetic-free gas bypassing the chamber, the proportion of vapour-containing gas and bypass gas being controlled by a tap.

## Slide 16: Factors affecting vaporiser output
Flow through the vaporising chamber
Efficiency of vaporization
Temperature Time
Gas flow rate
Carrier gas composition
Ambient pressure

## Slide 17: Breathing Circuits
Breathing circuits link the patient to the anaesthesia machine. Therefore, The function of the circuit is to; deliver Oxygen and anaesthetic gases to the patient, providing humidity and warmness to inspired gases, and to eliminate Carbon Dioxide.
Types of Breathing Circuit:
- Insufflation
- Open-Drop Anaesthesia
- Draw-Over Anaesthesia
- Mapleson's Circuits
- The Circle System

## Slide 18
INSUFFLATION: the blowing of anaesthetic gases across a patient’s face, avoiding direct connection between a breathing circuit and a patient’s airway. It used mainly in children.
OPEN-DROP ANESTHESIA: Ether or Chloroform dripped onto a gauze-covered mask, then applied to the patient’s face. Not used in modern medicine.
DRAW-OVER ANESTHESIA: nonrebreathing circuits that use ambient air as the carrier gas.
The insufflation and draw-over systems have several disadvantages:
- poor control of inspired gas concentration (poor control of depth of anesthesia)
- mechanical drawbacks during head and neck surgery
- pollution of the operating room with large volumes of waste gas

## Slide 19: Mapleson's Circuits
Is preferable than Insufflation and Draw-over systems; as it solves some of their disadvantages.
The relative location of these components determines circuit performance and is the basis of the Mapleson's classification.
Classified into 6 types (A, B, C, D, E, and F).
The main goal is to assist respiration and prevent rebreathing.

## Slide 20
Components:-
Corrugated Breathing Tubes made of either; rubber (reusable) or plastic (disposable) , this creates a low-resistance pathway and a potential reservoir for anesthetic gases.
Fresh Gas Inlet (FGI)
Adjustable Pressure-Limiting Valve (APL Valve, Pressure-Relief Valve, Pop-Off Valve) ; allows gases to exit the circuit as pressure rises.
- Open in Spontaneous Breathing
- Partially closed in Controlled Breathing
Waste-gas Scavenging System; for exiting gases.
Reservoir Bag (Breathing Bag); a reservoir for the anaesthetic gas, and a method for positive pressure ventilation.
Patient Connection (I.e., Face Mask)

## Slide 21
It consist of a three-way T-tube connected to the fresh gas outlet (F), a breathing bag (B) and a reservoir tube (R). The other end of the reservoir tube is connected to the patient (P) and a spring-loaded expiratory valve (V).

## Slide 22: Mapleson's A (Magill Circuit)
FGI is near reservoir bag, APL valve is near face mask.
The most efficient Mapleson's circuit for spontaneous ventilation.
Poor choice during controlled ventilation.
Enclosed Magill system is a modification that improves efficiency.
Coaxial Mapleson A modification (Lack's Circuit) provides waste gas scavenging.
Notes: Poor choice during controlled ventilation; a very high fresh gas flows (greater than three times minute ventilation) are required to prevent rebreathing with a Mapleson A circuit during controlled ventilation.

## Slide 23: Mapleson's B
FGI and APL valve are close to face mask (FGI being just distal to APL valve).
Fresh gas flows are conveniently available because the FGI is near the APL valve.
In order to prevent rebreathing fresh gas flow should be around 20-25L/min.
Mapleson's A is more efficient.

## Slide 24: Mapleson's C (Waters’ to-and-fro)
Similar to Mapleson's B, but it has a shorter breathing tube.
It does not have a corrugated tube.

## Slide 25: Mapleson's D
Interchanging the position of APL and FGI transforms Mapleson's A into D.
It is efficient during controlled ventilation; since fresh gas flow forces alveolar air away from the patient and toward the APL valve. This alters the fresh gas requirements.
It is also modified into Bain circuit.

## Slide 26: Bain Circuit
It is a popular modification of the Mapleson's D system.
A coaxial version of the Mapleson's D system that incorporates the FGI tubing inside the breathing tube.
This decreases circuit's bulk and retains efficiently the heat and humidity (inspired gas is warmed by the expired gas).
Disadvantage: the possibility of kinking or disconnection of FGI tube.

## Slide 27: Mapleson's E (Ayre’s T-piece)
Does not have an APL valve nor a Reservoir bag. FGI is near to patient's mask.
Exhalation tubing should provide a larger volume than tidal volume to prevent rebreathing. Scavenging is difficult.
Not good for spontaneous breathing.
Used for pediatric patients weighted up to 30 Kg.

## Slide 28: Mapleson's F (Jackson-Rees’ modification)
It is a Mapleson E with an open-ended reservoir bag connected to the end of the breathing tube (operator end) , it allows controlled ventilation and scavenging.
Does not have an APL valve.
Requires higher fresh gas flow.
Not good for spontaneous breathing.

## Slide 29: The Circle System
The Circle System aids the breathing system by avoiding the problems that are caused the Mapleson's circuits (as; waste of anaesthetic agent, pollution of the Operating Room, loss of patient's heat and humidity) and this is achieved by adding components to the breathing system, as:
- CO2 Absorber & Absorbent
- FGI
- Unidirectional Valves; Inspiratory & Expiratory
- Breathing tubes; Inspiratory & Expiratory
- Y-shaped connector
- APL Valve
- Reservoir Bag
- Right angle (90°) connector
- Ventilation Mask

## Slide 30
Carbon Dioxide Absorbent: to avoid hypercapnia upon rebreathing alveolar gas (reserves heat and humidity).
Soda Lime (more common) and Barium Hydroxide Lime are known absorbents.
Unidirectional Valves: contains a ceramic or mica disk resting horizontal on an annular valve seat, this prevents reflux of gas in the circuit.

## Slide 31
The essential features of the circle absorber are:
- Carbon dioxide absorber canister (C)
- Breathing bag (B)
- Unidirectional inspiratory (Vi) valve
- Unidirectional expiratory (Ve) valve
- Fresh gas supply (F)
- Pressure-relief valve (V)
N.B.
* The breathing system most used with anaesthesia machines is the Circle System.​
* Bain circuit is occasionally used.​

## Slide 32: Mechanical Ventilation
Ventilators generate gas flow by creating a pressure gradient between the proximal airway and the alveoli.
All modern anaesthesia machines are equipped with a ventilator, and they usually have the double circuit system design (Pneumatically powered and electronically controlled).
Older units relied on the generation of negative pressure around and inside the chest (e.g., iron lungs), whereas modern ventilators generate positive pressure and gas flow in the upper airway.
Types:-
- Positive Pressure Ventilators
- Negative Pressure Ventilators

## Slide 33: Positive Pressure Ventilators
The lungs are intermittently inflated by positive pressure generated by a ventilator, and gas flow is delivered to the airway.
Able to use endotracheal or tracheostomy tube.
Volume-cycled ventilation
The ventilator delivers a pre-set tidal volume regardless of the pressure generated.
Pressure-pre-set ventilation
The ventilator delivers a pre-set target pressure to the airway during inspiration. The resulting tidal volume delivered is therefore determined by the lung compliance and the airway resistance.

## Slide 34: Negative Pressure Ventilators (Iron Lungs)
Applied negative pressure around the body or thoracic cavity; the body of the patient is enclosed in an iron box or cylinder, and the patient’s head protruded out of the end.

## Slide 35: Humidification
Prevention of cilial damage and reduced drying of secretions.
As prolonged severe dehydration of the bronchial tree leads to encrustation of mucus and bronchial or endotracheal obstruction, particularly in neonates and patients with respiratory infection.
Humidifiers added to the breathing circuit minimize water and heat loss.
Prolonged humidification of gases by the lower respiratory tract leads to dehydration of mucosa, altered ciliary function, and, if excessively prolonged, could potentially lead to inspissation of secretions, atelectasis, and even ventilation/perfusion mismatching, particularly in patients with underlying lung disease.

## Slide 36
Types:-
Passive: The simplest designs are condenser humidifiers or heat and moisture exchanger (HME) units. They do not add heat or vapor but rather traps exhaled humidification and heat, which is released upon the subsequent inhalation.
Active: More effective in preserving moisture and heat. They add water to gas, by;
- passing the gas over a water chamber (pass-over humidifier)
- saturated wick (wick humidifier)
- bubbling through water (bubble-through humidifier)
- mixing it with vaporized water (vapor-phase humidifier)
Disadvantages of Humidifiers
- Disconnection
- Overheating
- Overhydration
- Infection
- Circuit resistance
- Interference with other devices

## Slide 37: Thank You